Pre-Live Session 2
Frequency domain/Spectral Density

---
House Appliances energy Data Set
- The data set is at 10 min for about 4.5 months. Data has 19735 rows.
- The house temperature and humidity conditions were monitored and measured every 3.3 min.
- Then, the data was averaged for 10 minutes periods.
- The energy data was logged every 10 minutes with m-bus energy meters.
- Weather from the nearest airport weather station (Chievres Airport, Belgium) was also collected.

---
House Appliance in Wh

---
Spectral Density

---
Spectral Density with different M values

---
Spectral Density Contd..
Frequencies: As you can see in the parzen window truncation, there appears to be some evidence of wandering behavior but there is also somewhat of a peak around 0.08 which could indicate a presence of frequency.
Because the data was only collected for 4 months, this could mean that there aren't any frequencies in the data or at least a very obvious one.
Based on the data, if we assume monthly frequency, then if we have 4 months then ¼ does not correspond with the peak shown in the spectral density which is at 0.08.

---
Takeaways
- Different trig function(realization) with same cyclic values at a time is evidence of non-stationary time series.
- Many realization are made up of various frequency component so if we can discover the frequency content of a data then we can better understand the process generating the data.
- Non-cyclic type functions can be expressed as a linear combination of sines and cosines.
- Fourier expansion is used for the estimation of ρ. |λ| is introduced to smooth the impact of k as k increases. So when k increases |λ| decreases. n-1 is replaced by M. M can be 2√n. M is designed to minimize the impact of autocorrelation as k goes to n. continues to work on minimizing the impact of larger autocorrelation.
- Spectra estimate for a cyclic function would have a peak at the frequency of the cyclic function.
- The Nyquist frequency is the highest observable frequency when sampling at the integers because you need at least 2 observations to observe one cycle.
- When sampling at the integers, a series with a frequency higher than 0.5 may become aliased with series with lower frequency.
λ_k

---
Questions
- Does the M value also applicable when calculating ρ value before applying it to the spectral density estimate.
- When we have multiple realizations in time series prediction model, do we avg the realization at each point and then build a time series model on the avg.
  I remember I had the last question the last time in class and it was clear to me at the time but I can’ seem to remember what the answer was.